## Slide 1
f
AJ SHRINK ERP
Flexible Packaging
Pouch Types & Specifications
Film Width · Repeat Length · Seal & Gusset Calculations
3 Side Seal
Center Seal
Standup / Zipper
Both Side Gusset
3D Flat Bottom
Confidential — Client Presentation

## Slide 2
5 POUCH TYPES — OVERVIEW
Film Width & Repeat Formulas at a Glance
#
Pouch Type
Film Width Formula
Repeat Length Formula
①
3 Side Seal
W + 2×Side Seal
H + Top Seal + Bottom Seal
②
Center Seal
W×2 + Center Seal Width
H + Top Seal + Bottom Seal
③
Standup / Zipper
W + 2×Side Seal
H + Top Seal + Gusset÷2
④
Both Side Gusset
W + 2×Side Gusset
H + Top Seal + Bottom Seal
⑤
3D / Flat Bottom
W + 2×Side Gusset
H + Top Seal + Bottom Gusset÷2

## Slide 3
①
3 SIDE SEAL POUCH
Three-sided sealed flat pouch — most common for snacks, spices, sachets
BODY
SIDE SEAL
TOP SEAL
BTM SEAL
← Film Width: W + 2×S →
↑ Repeat: H+Top+Btm ↓
DIAGRAM
FILM WIDTH (Across web direction)
Film Width = W + 2 × Side Seal
REPEAT LENGTH (Cylinder circumference direction)
Repeat = H + Top Seal + Bottom Seal
INPUT PARAMETERS
W — Pouch Width
e.g. 130 mm
H — Pouch Height
e.g. 200 mm
Top Seal
e.g. 10 mm
Bottom Seal
e.g. 8 mm
Side Seal (each side)
e.g. 10 mm
Film Width (total)
130 + 2×10 = 150 mm
💡 Film is folded at top — no seal needed there. Left, right, and bottom edges are sealed.

## Slide 4
②
CENTER SEAL POUCH
Film wraps around — sealed at center back, used for pillow packs & liquid sachets
A
B
CENTER SEAL
TOP SEAL
BTM SEAL
← Film Width: 2W + CenterSeal →
DIAGRAM
FILM WIDTH (Across web direction)
Film Width = 2W + Center Seal Width
REPEAT LENGTH (Cylinder circumference direction)
Repeat = H + Top Seal + Bottom Seal
INPUT PARAMETERS
W — Half Width (one side)
e.g. 80 mm
H — Pouch Height
e.g. 200 mm
Top Seal
e.g. 10 mm
Bottom Seal
e.g. 8 mm
Center Seal Width
e.g. 12 mm
Film Width (total)
2×80 + 12 = 172 mm
💡 W entered is HALF the pouch face width. Film wraps around body — both sides are the same printed panel.

## Slide 5
③
STANDUP POUCH / ZIPPER POUCH
Bottom gusset allows pouch to stand upright — premium snacks, pet food, beverages
BODY
GUSSET
TOP SEAL
← Film Width: W + 2×S →
↑ Gusset/2 in repeat ↓
DIAGRAM
FILM WIDTH (Across web direction)
Film Width = W + 2 × Side Seal
REPEAT LENGTH (Cylinder circumference direction)
Repeat = H + Top Seal + Gusset ÷ 2
INPUT PARAMETERS
W — Pouch Width
e.g. 150 mm
H — Pouch Height
e.g. 220 mm
Top Seal
e.g. 12 mm
Side Seal (each)
e.g. 10 mm
Bottom Gusset (full depth)
e.g. 60 mm
Film Width (total)
150 + 2×10 = 170 mm
💡 Gusset folds in half on the cylinder — repeat adds Gusset÷2. Zipper pouch same structure + zipper strip near top.

## Slide 6
④
BOTH SIDE GUSSET POUCH
Gusset on both sides for larger volume — rice bags, flour, heavy products
BODY
GUSSET
TOP SEAL
BTM SEAL
← Film Width: W + 2×SideGusset →
DIAGRAM
FILM WIDTH (Across web direction)
Film Width = W + 2 × Side Gusset
REPEAT LENGTH (Cylinder circumference direction)
Repeat = H + Top Seal + Bottom Seal
INPUT PARAMETERS
W — Pouch Width
e.g. 200 mm
H — Pouch Height
e.g. 300 mm
Top Seal
e.g. 15 mm
Bottom Seal
e.g. 12 mm
Side Gusset (each side)
e.g. 40 mm
Film Width (total)
200 + 2×40 = 280 mm
💡 Side gussets expand laterally for volume. Unlike standup — gusset is on sides (width direction), not bottom.

## Slide 7
WHY DIMENSIONS MATTER
How Pouch Measurements Drive Printing Costs
1
Film Width
Determines how many pouches fit ACROSS the film (AC UPS). More UPS across = fewer meters of film needed = lower cost per unit.
2
Repeat Length
Determines how many pouches fit around the cylinder (Repeat UPS). Correct seals & gusset in repeat = exact cylinder circumference match.
3
Seals & Gussets
Each seal & gusset adds real mm to the film requirement. Under-estimating = film short, machine stops. Over-estimating = wasted material.
4
Cylinder Selection
Cylinder circumference must be exact multiple of effective repeat. Wrong repeat = cylinder misalignment = 100% print rejection.

## Slide 8
AJ SHRINK ERP
Thank You
Flexible Packaging Solutions
5 Pouch Types · Accurate Planning · Zero Waste
Powered by AJ Shrink ERP

## Slide 9
⑤
3D POUCH / FLAT BOTTOM POUCH
Block-bottom design — side gussets + flat bottom gusset, premium coffee & tea
BODY
BTM GUSSET÷2
TOP SEAL
SIDE GUSSET
← Film Width: W + 2×SideGusset →
↑ Btm Gusset÷2 in repeat ↓
DIAGRAM
FILM WIDTH (Across web direction)
Film Width = W + 2 × Side Gusset
REPEAT LENGTH (Cylinder circumference direction)
Repeat = H + Top Seal + Bottom Gusset ÷ 2
INPUT PARAMETERS
W — Pouch Width
e.g. 180 mm
H — Pouch Height
e.g. 280 mm
Top Seal
e.g. 12 mm
Side Gusset (each)
e.g. 35 mm
Bottom Gusset (full depth)
e.g. 80 mm
Film Width (total)
180 + 2×35 = 250 mm
💡 Has BOTH side gussets (width) AND bottom gusset (length direction). Bottom gusset/2 adds to repeat. Premium block shape.