## Slide 1
Indas Analytics PVT.LTD.
Flexible Packaging
Pouch Types & Their Applications
Where they are used · What goes inside · Film & Cylinder Calculations
3 Side Seal
Center Seal
Standup / Zipper
Both Gusset
3D Flat Bottom
Client Presentation — Confidential

## Slide 2
INTRODUCTION
Why Choosing the Right Pouch Matters
The pouch type directly controls print area, material cost, and cylinder size
1
Film Width
Every pouch type adds SEALS or GUSSETS to the base width. This determines how many pouches fit ACROSS the film roll (AC UPS). More UPS across = lower cost per unit.
2
Cylinder Circumference
Seals + gussets added to height decide the exact cylinder circumference. Wrong measurement = cylinder won't divide evenly = print misalignment. Every mm counts for a ₹50,000+ cylinder order.
3
Material Waste
Incorrect seal allowance wastes film with every meter printed. 1mm error × 5,00,000 pouches = 500 meters of wasted film. Proper planning eliminates dead margin and side waste.
4
Structure for the Product
Heavier products need gussets. Liquids need tight center seals. Standing products need standup gussets. Premium products need 3D shape. Wrong structure = pouch fails on the filling line.
2 / 14

## Slide 3
OVERVIEW
All 5 Pouch Types at a Glance
Film Width formula · Repeat Length formula · Typical products
#
Pouch Type
Film Width
Repeat Length
Typical Products
①
3 Side Seal
W + 2×Side Seal
H + Top + Bottom Seal
Spices, sachets, namkeen, seeds, sugar, flour
②
Center Seal
2W + Center Seal
H + Top + Bottom Seal
Milk pouches, oil pouches, liquid sachets, shampoo
③
Standup / Zipper
W + 2×Side Seal
H + Top + Gusset÷2
Dry fruits, pet food, coffee, protein powder, snacks
④
Both Side Gusset
W + 2×Side Gusset
H + Top + Bottom Seal
Rice, atta, sugar (5kg+), cement additives, animal feed
⑤
3D / Flat Bottom
W + 2×Side Gusset
H + Top + Btm Gusset÷2
Premium coffee, tea, cosmetics, organic products
3 / 14

## Slide 4
①
3 SIDE SEAL POUCH
Simplest pouch — three sides heat-sealed, one side fold
BODY
SIDE SEAL
TOP SEAL
BTM SEAL
← W+2S = Film Width →
3 SIDES SEALED: Left + Right + Bottom
FILM WIDTH (across web):
Film Width = W + (2 × Side Seal)
REPEAT LENGTH (cyl. circumference):
Repeat = H + Top Seal + Bottom Seal
Example: W=130, H=200, Top=10, Btm=8, Side=10 → Film=150mm, Repeat=218mm
WHERE IS IT USED?
▸ Small retail pouches — 10g to 500g range
▸ Single-serve sachets — sugar, salt, spice, sauce
▸ Pharma — tablet strips, powder sachets
▸ Agricultural — seed packets, fertilizer sachets
▸ Industrial — adhesive sachets, lubricant pouches
WHAT PRODUCTS GO INSIDE?
• Namkeen / chips
• Spices (haldi, mirchi)
• Salt & sugar sachets
• Tea & coffee sachets
• Cement additives
• Seeds
• Sauce / ketchup
• Tablet pouches
• Detergent powder
• Seeds
TYPICAL FILM STRUCTURES USED
1. BOPP + CPP (most common for dry products)
2. PET + PE (higher barrier, good for moisture)
3. PET + AL Foil + PE (maximum barrier — pharma, spices)
4. BOPP + MET BOPP (shiny look — premium snacks)
💡 Most economical pouch — highest AC UPS possible. Side seal width 8–12mm typical. Use for anything dry and non-premium.
4 / 14

## Slide 5
②
CENTER SEAL POUCH
Film wraps around the product — sealed at the back center
A
B
CENTER SEAL
TOP SEAL
BTM SEAL
← 2W + Center Seal = Film Width →
Film wraps around — A & B are same printed panel
FILM WIDTH (across web):
Film Width = (W × 2) + Center Seal Width
REPEAT LENGTH (cyl. circumference):
Repeat = H + Top Seal + Bottom Seal
Example: W=80 (half), H=200, Top=10, Btm=8, Seal=12 → Film=172mm, Repeat=218mm
WHERE IS IT USED?
▸ Liquid pouches — milk, oil, drinking water
▸ Flow-wrap / pillow pack on HFFS machines
▸ Loose items — candy, biscuits, small hardware
▸ Bulk packaging — continuous film roll
▸ Instant noodles, bread — bakery flow wrap
WHAT PRODUCTS GO INSIDE?
• Milk (200ml, 500ml)
• Refined oil
• Drinking water
• Candy & toffee
• Biscuits
• Bread loaf
• Shampoo sachet
• Tomato sauce
• Noodles
• Ice cream
TYPICAL FILM STRUCTURES USED
1. PET + PE (standard liquid barrier — milk, oil)
2. LLDPE single layer (low-cost water pouches)
3. PET + MET PET + PE (oil, shampoo — high barrier)
4. BOPP + CPP (flow wrap — biscuits, candy)
💡 W entered is HALF the pouch face. Film Width = 2W+seal. HFFS machines use this structure — continuous film fed from roll.
5 / 14

## Slide 6
③
STANDUP POUCH / ZIPPER POUCH
Bottom gusset lets the pouch stand upright on shelf
BODY
GUSSET
TOP SEAL
SIDE
← W+2×Side Seal = Film Width →
Gusset÷2 folds into repeat length
FILM WIDTH (across web):
Film Width = W + (2 × Side Seal)
REPEAT LENGTH (cyl. circumference):
Repeat = H + Top Seal + Bottom Gusset ÷ 2
Example: W=150, H=220, Top=12, Side=10, Gusset=60 → Film=170mm, Repeat=262mm
WHERE IS IT USED?
▸ Retail shelf display — stands without support
▸ Premium FMCG — dry fruits, nuts, protein powder
▸ Pet food — kibble, treats, supplements
▸ E-commerce packaging — reusable with zipper
▸ Organic / health food — premium segment
WHAT PRODUCTS GO INSIDE?
• Dry fruits & nuts
• Protein powder
• Pet food & treats
• Coffee beans
• Quinoa & superfoods
• Washing powder
• Gummies & supplements
• Baby food (puffed)
• Makhana
• Seeds
TYPICAL FILM STRUCTURES USED
1. PET + AL Foil + PE (best barrier — coffee, protein)
2. BOPP + CPP (cost effective — snacks, dry items)
3. PET + MET PET + PE (metallic look — premium)
4. PET + PE with matte OPP (organic / natural look)
💡 Gusset/2 added to repeat — e.g. 60mm gusset adds 30mm to cylinder. Zipper pouch same as standup + zipper strip cut 20–25mm from top.
6 / 14

## Slide 7
④
BOTH SIDE GUSSET POUCH
Gussets on both sides expand laterally for high-volume products
BODY
SIDE GUSSET
TOP SEAL
BTM SEAL
← W + 2×Side Gusset = Film Width →
Gussets expand sideways for volume
FILM WIDTH (across web):
Film Width = W + (2 × Side Gusset)
REPEAT LENGTH (cyl. circumference):
Repeat = H + Top Seal + Bottom Seal
Example: W=200, H=300, Top=15, Btm=12, Gusset=40 → Film=280mm, Repeat=327mm
WHERE IS IT USED?
▸ Heavy grain packaging — 2kg, 5kg, 10kg bags
▸ Industrial products — chemicals, fertilizer, animal feed
▸ Bulk retail — atta, rice, dal, sugar
▸ Construction — tile adhesive, grout, putty
▸ Agriculture — seeds, pesticide powder
WHAT PRODUCTS GO INSIDE?
• Rice (2kg, 5kg, 10kg)
• Wheat flour (atta)
• Sugar & jaggery
• Dal & pulses
• Poha & dry grains
• Animal feed
• Fertilizer (IFFCO)
• Tile adhesive powder
• Cement admixture
• Seeds (bulk)
TYPICAL FILM STRUCTURES USED
1. BOPP + CPP (standard grain bags — rice, atta)
2. Woven PP laminate (heavy-duty — fertilizer, cement)
3. PET + AL + PE (moisture-sensitive — chemicals)
4. MET BOPP + CPP (shiny grain bags — premium rice)
💡 Unlike standup — gusset is on sides (width direction), not bottom. No gusset/2 in repeat. Higher film width per lane but simple repeat formula.
7 / 14

## Slide 8
⑤
3D POUCH / FLAT BOTTOM POUCH
Premium block-bottom — stands upright with a flat rectangular base
BODY
SIDE GUSSET
TOP SEAL
BTM FOLD
← W + 2×Side Gusset = Film Width →
3D block shape — stands + has flat base
FILM WIDTH (across web):
Film Width = W + (2 × Side Gusset)
REPEAT LENGTH (cyl. circumference):
Repeat = H + Top Seal + Bottom Gusset ÷ 2
Example: W=180, H=280, Top=12, Side=35, BtmGusset=80 → Film=250mm, Repeat=332mm
WHERE IS IT USED?
▸ Premium coffee & specialty tea — high street retail
▸ Cosmetics & personal care — serums, powders
▸ Gourmet food — imported chocolate, artisan products
▸ Organic & natural — quinoa, chia, health foods
▸ Gift packaging — premium dry fruits, sweets
WHAT PRODUCTS GO INSIDE?
• Ground coffee (250g)
• Specialty tea
• Premium chocolate
• Organic quinoa & seeds
• Turmeric latte powder
• Face wash powder
• Bath salts
• Protein isolate
• Premium dry fruits
• Herbal supplements
TYPICAL FILM STRUCTURES USED
1. Kraft paper + PE (sustainable / eco look — coffee)
2. PET + AL Foil + PE (maximum barrier — coffee freshness)
3. Matte OPP + CPP (soft-touch premium look)
4. PET + MET PET + PE (metallic premium — cosmetics)
💡 Both side gusset AND bottom gusset — most complex to plan. Bottom gusset/2 in repeat (like standup). Side gussets in film width. Premium product only.
8 / 14

## Slide 9
MATERIAL GUIDE
Film Structure Selection Guide
Which laminate to choose based on product type and barrier requirement
BOPP + CPP
Low cost · Good clarity · Seals well
Use for: Namkeen, biscuits, dry snacks, confectionery
⚠ Low barrier — not for moisture-sensitive products
PET + PE
Good strength · Medium barrier · Food safe
Use for: Milk, liquid pouches, oil (short shelf life)
⚠ Standard choice for most flexible pouches
PET + AL Foil + PE
Maximum barrier · Long shelf life · Light-proof
Use for: Coffee, spices, pharma, protein powder, chips
⚠ Most expensive — use only when shelf life > 6 months
PET + MET PET + PE
High barrier · Metallic look · Premium feel
Use for: Premium snacks, dry fruits, cosmetics
⚠ Good balance of cost and barrier for premium segment
Kraft Paper + PE
Eco look · Biodegradable appearance · Sustainable branding
Use for: Organic coffee, health foods, natural cosmetics
⚠ Lower barrier than foil — needs dry product
Woven PP Laminate
Very high strength · Heavy loads · Tear resistant
Use for: Rice (10kg+), fertilizer, cement, animal feed
⚠ Industrial use only — not for food contact without liner
9 / 14

## Slide 10
LIVE EXAMPLE
Complete Calculation Walkthrough
3 Side Seal Pouch — 130mm × 200mm — 1080mm machine
STEP 1
Enter Pouch Dimensions
Pouch Width (W) = 130 mm Pouch Height (H) = 200 mm Side Seal = 10 mm | Top Seal = 10 mm | Bottom Seal = 8 mm
STEP 2
Calculate Film Width
Film Width = W + 2 × Side Seal = 130 + 2×10 = 150 mm per lane (this is what 1 AC UPS occupies across the film)
STEP 3
Calculate Repeat Length
Repeat = H + Top Seal + Bottom Seal = 200 + 10 + 8 = 218 mm (this must divide evenly into cylinder circumference)
STEP 4
Calculate AC UPS
Machine Width = 1080 mm | Trim = 10mm each side Usable width = 1080 - 20 = 1060 mm AC UPS = floor(1060 ÷ 150) = 7 lanes
STEP 5
Select Cylinder
Cylinder Circ must be multiple of 218 mm: 218×1=218 | 218×2=436 | 218×3=654 mm Choose 436mm cylinder → 2 repeats per revolution
STEP 6
Total UPS & Film Usage
Total UPS = 7 AC UPS × 2 Repeat UPS = 14 pieces/rev For 1,00,000 pouches: ceil(1,00,000 ÷ 14) = 7,143 meters Film used: 7,143 m × 1060mm × GSM = X kg
10 / 14

## Slide 11
AVOID THESE
Common Mistakes in Pouch Planning
Errors that cause machine stops, cylinder rejection, or film waste
❌ Forgetting to add seals to film width
Seal width (8–12mm per side) MUST be added to W. Forgetting adds 16–24mm error per lane → 1–2 UPS less than expected.
❌ Not adding gusset/2 to repeat length
For standup & 3D pouches, gusset folds in half. Missing this = cylinder circumference is short → print misalign.
❌ Using pouch W as film width for center seal
Center seal: W is HALF width. Film = 2W + seal. Using just W gives 50% wrong film — machine cannot run.
❌ Confusing side gusset vs. bottom gusset
Both-side gusset → gusset in width direction (adds to film W). 3D Flat Bottom → gusset in both directions (adds to W and H).
❌ Cylinder circ not a multiple of repeat
Even 1mm off = print register error on every revolution. Always verify: cyl_circ % repeat_length < 0.5mm.
❌ Wrong structure type for product
Heavy product in 3-side seal = bag bursts on filling line. Liquid in standup without proper seal = leakage at gusset junction.
11 / 14

## Slide 12
OUR SOLUTION
How AJ Shrink ERP Automates All This
Select pouch type → enter dimensions → system calculates everything automatically
1
Auto Film Width
Select pouch type and the system auto-applies the correct formula. 3 Side = W+2S | Center = 2W+S | Gusset = W+2G No manual formula — zero calculation errors.
2
Auto Repeat Length
Top seal, bottom seal, and gusset/2 are all added automatically. The system picks the correct formula per pouch type. Cylinder circumference is verified as exact multiple.
3
Live UPS Planning
Enter machine width and trims — system shows all valid plans. AC UPS across × Repeat UPS = total pieces per revolution. Best plan highlighted automatically (least waste, most UPS).
4
Cylinder Matching
Real cylinder stock checked first (±1mm tolerance). If no stock match → special order cylinder auto-suggested. Sleeve-based or cylinder-direct planning — both supported.
5
Dimension Diagram
Visual diagram shows exact film zones — seals, gussets, body. Instant feedback as you type dimensions. Client presentations — show exactly what will be printed.
6
Cost Estimation
Film cost, ink cost, cylinder cost, machine time — all calculated. 3 quantity breakdowns (Q1/Q2/Q3) in a single view. Export to catalog → order → work order in one flow.
12 / 14

## Slide 13
SUMMARY
Which Pouch for Which Product?
Quick decision guide for sales & estimation teams
Pouch Type
Cost
Barrier Req
Resealable
How it Stands
Best For
3 Side Seal
Low
Low–Medium
No
Flat only
Sachets, spices, seeds, snacks, pharma
Center Seal
Low
Low
No
Flat / flow
Milk, oil, water, sauce, candy, noodles
Standup Zipper
Medium
Medium
Yes
Stands up
Dry fruits, coffee, pet food, protein
Both Gusset
High
Medium
No
Flat+gusset
Rice, atta, fertilizer, bulk grains
3D Flat Bottom
Premium
Medium
Optional
Block base
Premium coffee, tea, cosmetics, organic
13 / 14

## Slide 14
INDAS ANALYTICS PVT.LTC.
Thank You
· Complete ERP Solution
5 Pouch Types · Auto Film Calculation · Cylinder Planning · Cost Estimation
3SS
CS
SUP
BSG
3D